## Slide 1
Chapter 2 – Safety in Welding

## Slide 2: Who is responsible for a safe workplace?
Occupational Safety and Health Association (OSHA)
National Institute for Occupational Safety and Health (NIOSH)
Hazard Communication Standard (HCS)
Material Safety Data Sheets (MSDS)

## Slide 3: What was OSHA created to do?
To prevent work related injuries, illnesses and deaths by issuing and enforcing rules (called standards) for work place safety and health.

## Slide 4: National Institute for Occupational Safety and Health (NIOSH)
Is a research agency whose purpose is to determine the major types of hazards in the work place and ways of controlling them

## Slide 5: Hazard Communication Standard (HCS)
OSHA’s program that requires development of a hazard communication program whereby all employers with hazardous chemicals in their work place must have labels and MSDS sheets for their workers

## Slide 6: Material Safety Data Sheets (MSDS)
(MSDS) sheets contain information such as physical data (melting point, boiling point, flash point, etc..), toxicity, health effects, first aid, reactivity, storage, disposal, protective equipment, and spill-handling procedures.

## Slide 7: Who sets the standard by which all welding equipment should be manufactured by???
ANSI
(American National Standards Institute )

## Slide 8: How can an employer meet hazard requirements?
Hazardous Materials Identification System (HMIS)
Personal Protective Equipment (PPE)

## Slide 9: Four color codes used by HMIS simplify identification of the types of hazards and the colors they represent:

## Slide 10
A number designation signifies the degree of hazard level:
4 | Extreme
3 | Serious
2 | Moderate
1 | Slight
0 | Minimal

## Slide 11
The white label designating personal protective equipment uses a letter designating the appropriate personal protective equipment employees should wear while handling the material
A | safety glasses
B | safety glasses and gloves
C | safety glasses, gloves and an apron
D | face shield, gloves and an apron
E | safety glasses, gloves and a dust respirator
F | safety glasses, gloves, apron and a dust respirator
G | safety glasses, a vapor respirator
H | splash goggles, gloves, apron and a vapor respirator
I | safety glasses, gloves and a dust/vapor respirator
J | splash goggles, gloves, apron and a dust/vapor respirator
K | airline hood or mask, gloves, full suit and boots
L-Z | custom PPE specified by employer

## Slide 12: What types of clothing are recommended for welding?
Flame resistant wool or cotton material
Dark clothing is preferred over light colors
Leathers or a flame resistant shop coat or apron for out-of position welding and for high amperage applications

## Slide 13
flame resistant jacket, wool welding hat, high top leather safety shoes, and a passive style welding helmet
leather jacket, gauntlet style welding gloves, insulating heat shield and an auto darkening welding helmet

## Slide 14: Are there any types of clothing that should not be worn?
Nylon, polyester, and rayon clothing
Do not wear frayed clothing
Open toe shoes
Shorts

## Slide 15: What types of protection are required for hands and feet?
Hands
  Gauntlet style welding glove
  Lighter weight gloves
Feet
  High top steel toe boots

## Slide 16: What types of head protection are needed?
Welding helmet
Welding hat made of a flame resistant material
Ear plugs

## Slide 17: What eye protection is required for welding?
Safety glasses
Welding helmet
Full face shield for grinding, cutting and oxy-fuel welding

## Slide 18: Arc Flash
Ultraviolet light rays produced by the welding arc can damage the welder’s eyes. Exposure of the eyes to arc rays can result in a burning and blistering of the sensitive membrane of the eye.
(Note) Arc flash may take several hours to cause discomfort.

## Slide 19
Recommended Lens Shades For The Common Arc Welding Processes

## Slide 20
Recommended Lens Shades For Oxy-Fuel Cutting and Welding

## Slide 21: What are the electrical hazards for the welder?
Primary Input Power
  Is used to operate the welding power source and electrical tools (grinders, drills, radios, etc). It is always in the form of alternating current.
Secondary Welding Output
  Is the current flow used to arc weld. The amount of flow is controlled by the welding power source.

## Slide 22: What is the significance of properly grounded connections?

## Slide 23: For safety, in case of electrical wire damage, all electrical equipment must be grounded

## Slide 24: What is the significance of secondary welding output?
Electrical current flow of a Gas Metal Arc Welding circuit

## Slide 25: Important Steps For Electrical Safety
Keep body and clothes dry!
Never weld while standing in or having contact with water or damp surfaces!
Repair or replace damaged or worn insulators!
Never operate ungrounded equipment with non-insulated cases!
When you are done welding always remember to turn your machine off.